The following diagram shows the GIPO pin layout for the raspberry pi. The even number pins are by the edge of the board, with pin 1 and 2 being closes to the corner.

Your raspberry pi should be disconnected from power to make the pin connections.
The servos on the gimbal need to be connected in this order:

The top servo on the gimbal provides vertical movement (up and down) and it should be connected
- orange wire to pin 7 (GPIO 4)
- red wire to pin 4 (5V power)
- brown wire to pin 6 (Ground)

The bottom servo on the gimbal

- orange wire to pin 11 (GPIO 17)
- red wire to pin 2 (5V power)
- brown wire to pin 9 (Ground)

Now you can boot your pi by connecting power again.
Connect to the pi via putty
Install package that support GPIO communications: sudo apt-get install rpi.gpio
Start the vnc server on the pi: vncserver

From the laptop use the VNC client to connect to the pi

Use web browser on the pi to access connectionblocks.com
Pull down the gimbal-pi.tgz file

From command line on the pi
- cd ~/
- decompress this file: tar -xzvf Downloads/gimbal-pi.tgz
- This will create the directory gimbal-pi
- Change into this directory via: cd gimbal-pi

Run the following from the pi command line to verify your servos are working
- ./vert-tst.py
- ./horz-tst.py

The gimbal should have moved in both the horizontal and vertical directions, if not talk with the mentor!!

Next we want to enable the camera: sudo raspi-config
- Select: Interfacing Options
- Select: P1 Camera
- It will ask to enable camera select: Yes
- It’ll tell you the camera is enabled select: OK
- Select: Finish
- It’ll ask if you want to reboot, select: Yes
Use putty to get back into the pi

Next we want to install packages to enable web access to the camera.
At the pi command line Grab the software:
    git clone https://github.com/silvanmelchior/RPi_Cam_Web_Interface.git

Get into the directory you just pulled down: cd RPi_Cam_Web_Interface

Make sure you have the newest list of packages: sudo apt-get update

Install the application: ./install.sh
- When the menu pops up hit the tab key to get to <OK> then hit the Return/Enter key
- It should ask if you want to start the camera, select: Yes

If things are working correctly the light on the camera should come on and the camera should now be available via the web interface, from the web browser on your laptop. Surf to the IP address/html of your Raspberry pi and you see something like this:

The last step is to add controls for the gimbal to this interface.
At the pi command line: cd ~/gimbal-pi
Copy of some file: sudo cp *.sh /var/www/html/macros/
Make sure they have proper ownership:
sudo chown www-data: /var/www/html/macros/*.sh
Add buttons to web interface: sudo cp userbuttons /var/www/html/

At your laptop browser where you have the web camera up hit the refresh button and you should see 4 new buttons on the screen.

We need to start the application that responds to these buttons
At the pi command line enter: ~/gimbal-pi/networkControlGPIO.py